## Slide 1: Custom download tools Q&A
Hardware Development --- Tools Group
Lu Junhui

## Slide 2: Brief introduction
Common problem solving
log crawling content

## Slide 3: Please update the tool version to the latest version
SMT、 Assembly Factory Tool Location ：
\\192.168.1.71\研发生产工具\00_FactoryRelease\03_SWD
R & D center tool location ：
\\192.168.1.71\研发生产工具\02_SWTesting\02_SoftwareDownload
E.g：Release Notes：v3.1702.09.10 February 9, 2017 at 10 o'clock
ftp://ftp.reallytek.com/
account number ：gongjuftp
password：jkl,./234
FTP access：
IP access ：
IP access without permission, you can use FTP access, as follows ：

## Slide 4: Version type introduction – The specific use and reference operation document
For R&D center , there are different functions to select
SoftwaredownloadvX.XXXX.XX.XX_for_Development_Center
For assembly factory, Upgrade download with retaining nv
SoftwaredownloadvX.XXXX.XX.XX_for_FirmwareUpgrade
For SMT factory, format download with erasing nv
SoftwaredownloadvX.XXXX.XX.XX_for_FormatAllandDownload
For automation group, command line mode
SoftwaredownloadvX.XXXX.XX.XX_for_Software_Automatic_Test
For After-sales center , a variety of modes can be chosen
SoftwaredownloadvX.XXXX.XX.XX_for_AfterSales

## Slide 5: Common problem solving
When a mobile phone inserts , but tool has no response
MTK driver installation is abnormal
Version checksum failed
Software version mismatch
DA connection failed
Failed to download on the halfway

## Slide 6: Abnormal problem handling one ： Mobile phone insertion tool no response
Mobile phone insertion tool no response
Check the phone's connection to the computer's USB port
Is there any other program occupying the MTK port?
Device Manager port?
no
yes
Insert the USB cable directly,Normal download mode
Volume keys + insert USB cable; forced download mode; If the volume can not enter the key, you can ask the software-driven or hardware colleagues.
Format download 、fuse operation：
Firmware upgrade：
Whether the driver is installed correctly

## Slide 7: Abnormal problem handling two ： MTK driver installation is abnormal
Some colleagues phone into the computer after the port appears in the form of a small yellow exclamation mark at the port, indicating that the driver installation is abnormal, you need to reinstall 。
Driver version 3.0.1504.0 and above is required
Drive path and version can be obtained in the same path

## Slide 8: Driver reloading method is as follows ：
First step
Second step
Third step

## Slide 9: Abnormal problem handling three ：version CheckSum failed
Version verification failed
Use the checksum tool to regenerate
Check if the file matches the version
Checksum file version?
no
yes

## Slide 10: Abnormal problem handling four ： Software version does not match
Figure above, this error message shows that the software version in the phone is inconsistent with the local software version on pc.
Check that the version you want to download is exactly the same as the phone model. Especially for X600 and X600M such easy to make mistakes.

## Slide 11: Abnormal problem handling five ： DA connection failed
There are two main types of situations:
1）DA permissions are incorrect
Mobile phone has efused, but the software version is not efused , please check whether to put “efuse_MTxxxx.xml”file in the sw version.
2）Abnormal phone status Long press the phone power key to reset the phone

## Slide 12: Abnormal problem handling six:failed to download halfway
There are two main types of situations:
1） Phone battery is low, please download the phone to ensure that more than 10% of the electricity. please be sure to maintain external power supply with Motherboard download, .
2）Whether the connection between the phone and the computer is stable can be verified by replacing the USB cable or the USB connector on the back of the computer.

## Slide 13: Log crawling content
Download tool failed screenshot （Emphasize full screen）
Tools directory Testlog

## Slide 14: Log crawling content one:Download tool to cut full screen

## Slide 15: Log crawling content two：TestLog Catalog package

## Slide 16: Q&A Thanks
www.transsion.com